## Slide 1: Transit Route Planning & Remix Transit Planning Tool
Rob Smith
AVP, Service Planning & Scheduling, DART
MAX Dallas Visit
May 2, 2019

## Slide 2: Transit Planning Overview
Transit planning involves the development of plans and proposals for future service development
Over the years, the planning field has split into two separate tracks: long-range capital planning and shorter-range service planning
At DART, the capital planning and service planning functions have separate staff and focus, though we work cooperatively
This presentation is focused on the service planning side of the equation

## Slide 3: Capital and Service Planning
CAPITAL PLANNING
Longer-range focus – more than five years
Tending to address major capital investments like rail and bus rapid transit
Computing tools tend to focus on travel demand forecasting and other activities tied to longer-term analysis
SERVICE PLANNING
Shorter-range focus – usually less than five years
Tending to address bus service changes and items that will happen in the next few service changes
Computing tools tend to focus on ridership analysis, schedule development, geographic information systems (GIS), and other spatial analysis tools

## Slide 4: Service Planning & Scheduling at DART
Staff of 21 positions, most currently filled
Four key focus areas:
  Service planning – management of the service change process and development of plans and proposals for service changes, also manages bus stop program
  Scheduling – scheduling of buses and trains, including development of service timetables and operator work assignments
  Service analysis – analysis of ridership, geospatial data, and other topics that support DART activities
  Innovative services – management of our vanpool program and other contracted service arrangements with a series of partners (as a part of our Site-Specific Shuttle program)

## Slide 5: Service Planning at DART
Other staff within the Service Planning group manage miscellaneous construction contracts, on-street facilities, traffic signal priority programs, and other projects

## Slide 6: Service Planning Process
Policies: Service Standards and other Board-determined policies that guide planning and evaluation of DART services
Data & Analysis: Detailed collection and analysis of data on ridership, service performance, schedule performance, and other issues
Feedback: Communication with external and internal customers on service-related issues, some ongoing, others as a part of specialized meetings

## Slide 7: Service Planning Process
Plans: Development of 5-year Service Plans and other planning efforts to direct future service changes
Service Changes: Development of proposals for service changes several times per year, along with management of the process
Implementation: Schedule service, prepare information for other internal customers, etc.
Evaluation: Review of implemented service plans to see if they meet ridership and performance goals

## Slide 8: Data & Analysis: Key to All Efforts
Because of the inherent complexity of transit service and ridership, transit service planning is a data-driven endeavor
Collection and analysis of data are core parts of the process
Specialized geospatial analysis is more frequently used now to support planning efforts, and specialized tools have evolved to support planning efforts
The rest of today’s presentation will look at this issue in greater detail

## Slide 9: Evolution of Data Analysis for Service Planning
My transit career started in April 1982, and a lot has changed in the past 37 years
Capabilities for data collection and analysis have grown dramatically over that time…

## Slide 10: Computing
1982
Apple IIe computers were just starting to be used in transit environments
64k RAM
Floppy disc drives for programs and storage
Primitive monochrome screens with minimal graphical capability
Planners rarely had desktop use of computers
2019
Advanced desktop and laptop PC systems with cloud computing support
8+ Gb RAM
Fast SSD and/or hard disk storage with cloud elements
Advanced graphics capabilities for mapping, GIS, and other functions
Computers are a normal desk tool for Planners (and everyone)

## Slide 11: Mapping/Geospatial Analysis
1982
Hand-drawn maps traced from city maps using a light table
Colored city maps to show demographics and other characteristics, again with hand-drawn routes
2019
Full GIS capabilities for map drawing, geospatial analysis, and many other uses
Specialized tools like Remix, Urban Footprint, and a number of others to support geospatial analysis and planning activities

## Slide 12: Data Collection
1982
Ridership counts by bus operators
Manual ride and point check data collection by surveyors in the field
2019
Automatic passenger counters on buses and trains
Detailed on time performance data through automatic vehicle location systems and other means
Real-time review and playback of actual bus/train operations
Customer interviews collected and processed using tablets

## Slide 13: Presentations
1982
If done, slide presentations were prepared on film slides by graphics companies and shown on carousel slide projectors
Hand-drawn maps, occasionally supplemented by more professional work done by graphic artists
2019
Has PowerPoint really improved anything?
Items are much easier and quicker to produce

## Slide 14: Remix: An Example of the Evolution
Remix is specialized, cloud-based software that supports service planning functions, including:
  Drawing and creating routes
  Rudimentary scheduling capabilities
  Costing of service proposals
  Geospatial analysis of demographic and other data vis-à-vis current and proposed routes
  Quick review of travel time access over the network
  New features have been added on a regular basis

## Slide 15: What Does Remix Offer?
The ability to quickly develop and analyze different service alternatives – much more quickly than through other tools of the past
Detailed demographic, job access, and other information is available for routes and networks under consideration
Quick costing of service alternatives

## Slide 16
This is a simple example I used to cost out a route. It took less than 10 minutes to draw and calculate cost and basic impacts

## Slide 17: More Complex Example: Grid System Analysis
We have had a lot of questions about development of a grid system for DART service
The City of Dallas passed a resolution asking DART to develop a high-frequency grid bus route network
Remix gave us a way to draw and analyze the potential impact of a grid system relatively quickly
Results were exportable into GIS for even more analysis of impacts

## Slide 18: DART Grid Network Concept: Financial Implications
Frequency improvements have a significant impact on costs
604 peak local buses required vs. 484 now (not including spares)
Fleet expansion would require a new operating facility
65% increase in revenue hours over existing service levels
$72m in additional operating costs over current service

## Slide 19: DART Grid Network Issues
Significant difference in coverage – existing route network shown in red
Some low income areas with high transit dependency do not have grid arterials, and would lose significant service coverage
Trinity River and lakes break grid street network, with impacts on connectivity (e.g. Pleasant Grove to Oak Cliff)

## Slide 20: Analyzing Impact of Changes: Job Access
Our newest Service Standards include a goal of improving job access for service changes
Remix allows quick analysis for different locations in the service area through something called the “Jane” tool

## Slide 21
Additional Jobs Accessible Within 60 Minutes: August Service Changes
Data: U.S. Census Longitudinal Employer Household Dynamics (LEHD) 2015
Average increase for these locations: 6.1%

## Slide 22: Remix Demo

## Slide 23: Remix Limitations
It is not currently structured to deal with demand-responsive services, and DART is looking for that capability
Service costing does not fully work the way transit agencies typically calculate costs, but we have found that the differences are not great enough to worry

## Slide 25: DART GoLink Service
Rob Smith
AVP, Service Planning & Scheduling, DART
MAX Dallas Visit
May 2, 2019

## Slide 26
Mobility Services
Connected Services
APPS + Services
Multimodal Services
Dynamic Car Pooling
Bike Sharing
Smart Payments
Real-Time Information
Rewards + Incentives
Trip Planning
P3 Agreements
Car Sharing
Transit
Dynamic Parking
Traffic Management
Automated Vehicles
WiFi
Microtransit
Taxi
TNCs
Interactive Kiosk
Car
Companies
CUSTOMER
Connected Traveler
System Integrations
Data Hubs
Communications
Analytics
DART’s Mobility as a Service Framework
Currently in process
Not currently in process
Paratransit
Air Taxi
Scooters

## Slide 27: Mobility on Demand/GoLink
The Mobility on Demand (MoD) pilot project builds upon a federal “Sandbox” grant, providing integration of public and third-party mobility providers
Zoned service accommodates ”last mile” access to/from other DART services and within-zone circulation
All zones will include a mix of dedicated vehicles under the GoLink brand, private carriers, and DART subsidy and management

## Slide 28
GoLink Service

## Slide 29: GoLink Service
The primary first mile/last mile service has been branded as GoLink service
GoLink replaces and expands upon our older On Call demand-responsive service program
GoLink service has been expanded to 6 additional zones
Several of these areas had limited or no service
13 GoLink zones are in operation
We are actively looking at 9 to 11 other candidate zones for future expansion

## Slide 30: GoLink Functions
FIRST/LAST MILE OPERATION
All zones connect to DART rail or express bus service for access to the rest of the system
INTERNAL CIRCULATION
Offering circulation service for shopping, school, medical appointments, or other needs

## Slide 31: Transition: On Call to GoLink
ON CALL SERVICE
7 zones, replaced low-performing fixed-route services
1 dedicated, assigned vehicle in most zones (2 if needed)
Peak service restricted to trips to/from the anchor point
Circulation trips within the zone midday and early evening only
In order to allow for the single vehicle operation, most zones were 6 square miles per less
Telephone reservations one hour in advance
GOLINK SERVICE
6 new ones added in areas without fixed-route coverage
Mix of dedicated vehicles and TNC support through UberPool
No travel restrictions within zones or to/from anchor point
Some zones are much larger and use multiple vehicles – up to 23 mi.2
App users do not have to book trips in advance – our goal is to pick up customers 10-12 minutes after their booking

## Slide 32
OnCall program included 7 zones
Service available where local fixed-route service did not perform to standards
On Call Program

## Slide 33
13 zones now in full GoLink operation
GoLink Final:
March 2019

## Slide 34
Service Planning staff are looking at potential expansion of the program
New zones target low productivity fixed route and/or FLEX services
Opportunities

## Slide 35: Role of TNC’s
We have traditionally operated On Call using dedicated vehicles assigned to each zone
Our goal with GoLink service is to integrate TNC’s to keep per passenger costs down and to expand capacity
UberPool is our first TNC partner for GoLink, and we have started a pilot project in 6 zones
Right now the experience is somewhat limited until UberPool trips can be directly scheduled in our app – customers who wish to use it must go to the Uber app to book trips
Our new operating contract will allow us to move away from having some of the dedicated vehicles we have been operating

## Slide 36: Rider Response
Overall ridership levels are very dependent upon activities and characteristics of each zone
Where On Call service has transitioned to GoLink, we have generally seen significant ridership growth

## Slide 37: GoLink Ridership: Plano/Rowlett
Legacy West: 131
F.N Plano: 39
N.C. Plano: 121
Rowlett: 125
Chart: Average Weekday Ridership
| Legacy West | N.C.Plano | Rowlett | F.N.Plano
Column2 | 131 | 121 | 125 | 39

## Slide 38: GoLink Ridership: Southern Sector
Inland Port: 47
Rylie: 24
Kleberg: 76
Chart: Average Weekday Ridership
| Inland Port | Kleberg | Rylie
Column2 | 47 | 76 | 24

## Slide 39: GoLink Transition: Rylie/Kleberg
Chart: February Effect of Service Modifications – Route 842 vs. GoLink Average Weekday Ridership
| Route 842 (Feb 2018) | Kleberg/Rylie
2018 | 69 | 92
33.4% Increase

## Slide 40: GoLink Transition: NC Plano
Chart: February Effect of Service Modifications – North Central Plano GoLink vs. DART-on-Call
| DART-on-Call (Feb. 2018) | GoLink
2018 | 81 | 132
63.0% Increase

## Slide 41: GoLink Transition: Rowlett
Chart: February Effect of Service Modifications – Rowlett GoLink vs. DART-on-Call
| DART-on-Call (Feb. 2018) | GoLink
2018 | 45 | 137
204.4% Increase

## Slide 42: UberPool Weekly Ridership Trends
Chart: 
| Week of 3/11/19 | Week of 3/18/19 | Week of 3/25/19 | Week of 4/1/19 | Week of 4/8/19
Riders | 212 | 369 | 461 | 493 | 591

## Slide 43: Customer Satisfaction Survey Results
Chart: 
| (no answer) | Average | Excellent | Good | Poor | Very Poor
Total | 23 | 29 | 130 | 69 | 3 | 1

## Slide 44: Key Program Goal: Cost Effectiveness
We are working to keep program costs at a reasonable level – targeting $12.00-12.50 per passenger as our goal
Mixed operation of dedicated vehicles and TNC’s will be crucial in reaching that goal

## Slide 45: GoLink Trends Subsidy/Rider, No UberPool
Chart: 
| 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525
Cost/Rider | 21.27 | 18.54 | 18.53 | 18.7 | 18.19 | 17.07 | 16.73 | 15.98 | 16.92 | 17 | 16.91 | 18.3

## Slide 46: UberPool Weekly Subsidy/Rider
Chart: 
| Week of 3/11/19 | Week of 3/18/19 | Week of 3/25/19 | Week of 4/1/19 | Week of 4/8/19
Cost/Rider | 4.02 | 5.54 | 5.12 | 4.86 | 4.96

## Slide 47: Conclusion
We are very encouraged with what we have seen so far
Work remains to fully integrate TNC operations and maintain good performance (e.g. wait times)
Expansion expected in the future